## Slide 1
Computer Vision
PDS
SDN
NFV
https://www.youtube.com/@AmelOline/videos
https://github.com/siagianp
https://github.com/amelcharolinesgn2/IoT_simulator-mqtt-NodeRed
https://github.com/amelcharolinesgn2/Cloud-Infrastructures
https://github.com/amelcharolinesgn2/ClouD-Infrastructure-SISKA-2025
11_10. Filter Aktif
Notes: http://www.sophphx.caltech.edu/Physics_5/Experiment_6.pdf
https://ocw.mit.edu/ans7870/RES/RES.6-010/MITRES_6-010S13_comchaptrs.pdf

## Slide 2: Multivibrator
Capaian :
Mampu memahami perancangan filter menggunakan op-amp untuk berbagai jenis filter
https://ocw.mit.edu/courses/6-01sc-introduction-to-electrical-engineering-and-computer-science-i-spring-2011/resources/op-amps/
Filter Aktif
Notes: https://unacademy.com/lesson/low-frequency-analysis-of-bjt-amplifier/5TUKWO6Z
https://ocw.mit.edu/courses/6-01sc-introduction-to-electrical-engineering-and-computer-science-i-spring-2011/resources/op-amps/

## Slide 3
Filter Aktif
Perancangan Filter Aktif

## Slide 4
Filter: suatu alat yang memiliki fungsi untuk melewatkan frekuensi tertentu.
Filter analog berarti filter yang melewatkan sinyal analog dan pengolahan sinyalnya juga dilakukan secara analog
Berdasarkan komponen penyusunnya, filter analog dibagi:
    Filter LC pasif
    Filter RC aktif
BAB III FILTER ANALOG
Filter Aktif
Filter Aktif

## Slide 5
Berdasarkan daerah frekuensi yang dilewatkan, filter analog dibagi menjadi
    LPF (Low Pass Filter)
    BPF (Band Pass Filter)
    HPF (High Pass Filter)
    BSF/BRF (Band Stop Filter/ Band Reject Filter)
BAB III FILTER ANALOG

## Slide 6
Berdasarkan bentuk respon frekuensi terhadap gain:
    Filter Butterworth (maximally flat)
    Filter Chebyshev (Tchebycheff)
    Filter Bessel (Maximally Flat Time Delay)
    Filter Elliptic
BAB III FILTER ANALOG

## Slide 7
Berdasarkan sifat penguatannya, filter bisa diklasifikasikan:
  Filter aktif : bersifat menguatkan
    Komponen penyusunnya: penguat, RC.
    Keuntungan: lebih kecil, ringan, murah dan fleksibel.
    Kekurangan: catu daya eksternal, lebih sensitif, dan frekuensi kerja yang tidak terlalu tinggi (ratusan MHz).
  Filter pasif : bersifat tidak menguatkan
    Komponen penyusunnya : RLC
    Kelebihan: untuk frekuensi tinggi, tidak diperlukan catu daya
    Kekurangan: dimensi lebih besar, loss pada daerah passband
BAB III FILTER ANALOG

## Slide 8: Keuntungan filter aktif
Penguatan dan frekuensinya mudah diatur
Tidak ada masalah beban, karena tahanan input tinggi dan tahanan output rendah.
Harga, lebih ekonomis

## Slide 9: Filter Aktif LPF Orde 1
Perancangan Filter Aktif

## Slide 10
Notes: Untuk frekuensi cut off 1KHz

## Slide 11: Filter Aktif LPF Orde 2

## Slide 13
Notes: Untuk frekuensi cut off 1kHz

## Slide 14: Perbandingan LPF Orde 1 dan Orde 2

## Slide 15: Perancangan
Rancanglah LPF orde 3 Butterworth dengan frekuensi sebesar 1kH dari tabel berikut:

## Slide 16: Filter Aktif HPF Orde 1

## Slide 17
Notes: Frekuensi 1KHz

## Slide 18: Filter Aktif HPF Orde 2

## Slide 19
Notes: Frekuensi 1kHz

## Slide 20: Perancangan
Rancanglah HPF orde 3 Butterworth dengan frekuensi sebesar 1kH dari tabel berikut:

## Slide 21: Filter Aktif LPF Orde 1 Butterworth dengan Penguatan

## Slide 22: Filter Aktif LPF Orde 2 Butterworth dengan Penguatan

## Slide 23: Filter Aktif HPF Orde 1 Butterworth dengan Penguatan

## Slide 24: Filter Aktif HPF Orde 2 Butterworth dengan Penguatan

## Slide 25: Filter LPF Orde 2 Chebyshev 3 dB

## Slide 26: Filter HPF Orde 3 Chebyshev 0.1dB

## Slide 27
Thank You !!
https://www.youtube.com/@AmelOline/videos
https://github.com/siagianp
https://github.com/amelcharolinesgn2/IoT_simulator-mqtt-NodeRed
https://github.com/amelcharolinesgn2/Cloud-Infrastructures
https://github.com/amelcharolinesgn2/ClouD-Infrastructure-SISKA-2025
Computer Vision
PDS
SDN
NFV
See the next

## Slide 28: HW
Lakukan analisis untuk umpan balik negatif bertikut:
Notes: https://ocw.mit.edu/courses/6-720j-integrated-microelectronic-devices-spring-2007/pages/lecture-notes/
https://ocw.mit.edu/courses/6-01sc-introduction-to-electrical-engineering-and-computer-science-i-spring-2011/resources/op-amps/