## Slide 1: 9.0_Electonic Component
Computer Vision
PDS
SDN
NFV
https://www.youtube.com/@AmelOline/videos
https://github.com/siagianp
https://github.com/amelcharolinesgn2/IoT_simulator-mqtt-NodeRed
https://github.com/amelcharolinesgn2/Cloud-Infrastructures
https://github.com/amelcharolinesgn2/ClouD-Infrastructure-SISKA-2025

## Slide 2: Signals, Circuits, and Computers

## Slide 3
CIRCUIT
Input
Output
Electronic Circuits and Components
An “Electronic Circuit “ is a combination of electronic components and conductive wires interconnected in a way as to achieve an outcome: - Achieve a current /voltage of a certain value (signal)
- Amplify a signal
- Transfer data
The purpose of an electronic component is to allow the designer to control the flow of current as to achieve a specified result/output.
(Resistors, Capacitors, Inductors, Diodes, Transistors )

## Slide 4
Electronic Components
Active Components (have directionality)
  Semiconductor devices-transistors
Passive Components (Have no directionality)
  Resistors, capacitors, inductors, diodes
  (diodes and polarized capacitors must be
  installed in a specified way)

## Slide 5
Resistors are passive elements that oppose/restrict the flow of current.
A voltage is developed across its terminal, proportional to the current through the resistor.
V = IR
Units: Ohms (Ω)
A. Resistors:
Electronic Components (cont.)

## Slide 6
B. Capacitors
behave like a tiny rechargeable battery. (store energy and release it later. )
are made of two parallel conductors separated by a dielectric.
are used for filtering, tuning, separating signals , etc.
The ability of a capacitor to store charge is called “Capacitance”
C = Q/V (amount of charge stored/applied voltage)
The unit of capacitance is the Farad. Commonly used capacitances are much smaller than 1 Farad, micro-Farads (10-6 Farad, μF),
nano-Farads (10-9 Farad, nF), pico-Farads (10-12 Farad, pF).
Electronic Components (cont.)

## Slide 7
Symbol for the NPN Transistor
Symbol for the PNP Transistor
Transistors are commonly used for signal amplification, switching, voltage regulation, etc.
base
emitter
collector
Transistors
Electronic Components (cont.)

## Slide 8
Diodes are semiconductor devices that allow
current in only one direction
Fuses are devices that protect the circuit from overload.
Are made of a wire that melts when the current through it exceeds a specified value
Electronic Components (cont.)

## Slide 9
Q5. Which of the following components used in a circuit stores energy?
Resistors
Inductors
Capacitors
Diodes
Transistors

## Slide 10
Q6. Which of the following components used in a circuit allows the current to flow one way
Resistors
Inductors
Capacitors
Diodes
Fuses

## Slide 11
LEDs- Light Emitting Diodes:
A special kind of diode: They allow current to flow in one direction.
The LED will light up when the proper amount of current passes through.
Electronic Components (cont.)
1-3
4
5

## Slide 12
Infrared Detectors
The appearance of these infrared photo detectors and the internal structure is similar to that of an LED.
The infrared photo detector has a focal direction, and the detection angle is about 15°. (8x15=120˚)
This small detection angle allows the controller to tell the direction where the infrared light comes from.
7
Electronic Components (cont.)
0
3

## Slide 13
Tuning CKT
Amplifier
Selector
Counter
Integrated Circuits
A small scale electronic CKT on a substrate
of semiconductor material
Orientation

## Slide 14: Robotic Component Functional Summary*
B. Motors
  Motors are devices that can transform electrical energy into mechanical energy.
  Control the movement/speed of the robot.
  Direction: CW or CCW.
  SWR Command:
    SetPWM[Port #, Direction & Speed# ]
  Range: Direction & Speed:
    000 CCW-High
    127 STOP
    255 CW - High
*E10 Manual-Vex Robotics Design System

## Slide 15
C. Servos
Servo motors are a type of motor that can be directed to turn to a specific direction, rather than just spin forward or backward.
Robotic Component Functional Summary (cont.)
SWR Command: SetPWM [ Port#, Direction Value]

## Slide 16
C. The Bumper
- The bumper switch is a digital sensor.
- It tells the robot whether the bumper on the front of the sensor is being pushed in or not.
Robotic Component Functional Summary(cont.)
SWR Command: bumperL = GetDigitalInput[Port#]
Input =1 (or 5V) when the bumper is not pushed.
Input =0 (or 0V) when the bumper is pushed.
5v
VEX
Digital
IO Port
0v
Input

## Slide 17
The limit switch (similar to Bumper SW)
  The limit switch is a digital sensor.
  It can tell the robot whether the sensor’s metal arm is being pushed down or not.
Robotic Component Functional Summary (cont.)
  When the limit switch is not being pushed in, the sensor maintains a digital HIGH signal on its sensor port. (1 or 5v.)
  When an external force (like a collision or being pressed up against a wall) pushes the switch in, it changes its signal to a digital LOW until the limit switch is released. (0 or 0v.)
SWR Command: GetDigitalInput[Port#]

## Slide 18
5v
VEX
Digital
IO Port
0v
Input
Q7. What is the state of the bumper input in Fig 1.?
a. Input =1 (or 5V).
b. Input =0 (or 0V)
Fig. 1.

## Slide 19
Robotic Component Functional Summary (cont.)
Ultrasonic range finder
An ultrasonic range finder sensor enables a robot to detect obstacles in its path by utilizing the propagation of high-frequency sound waves.
The sensor emits a sound wave, which bounces off a reflective surface and returns to the sensor. Then, using the amount of time it takes for the wave to return to the sensor, the distance to the object can be computed.

## Slide 20
The light sensor
The light sensor uses a photocell that allows your robot to detect and react to light.
Analog input of light levels:
Find dark or bright areas.
It uses a photoconductive photocells which are photo resistors, meaning that their resistance value changes based on the amount of incident light.
Robotic Component Functional Summary (cont.)

## Slide 21
Thank You !!
https://www.youtube.com/@AmelOline/videos
https://github.com/siagianp
https://github.com/amelcharolinesgn2/IoT_simulator-mqtt-NodeRed
https://github.com/amelcharolinesgn2/Cloud-Infrastructures
https://github.com/amelcharolinesgn2/ClouD-Infrastructure-SISKA-2025
Computer Vision
PDS
SDN
NFV