## Slide 1: 9.3_Transistor Amp
Computer Vision
PDS
SDN
NFV
https://www.youtube.com/@AmelOline/videos
https://github.com/siagianp
https://github.com/amelcharolinesgn2/IoT_simulator-mqtt-NodeRed
https://github.com/amelcharolinesgn2/Cloud-Infrastructures
https://github.com/amelcharolinesgn2/ClouD-Infrastructure-SISKA-2025

## Slide 2: What is a transistor?

## Slide 3: BJT Transistors:
NPN Transistor
PNP Transistor
Sandwiching a P-type layer between two n-type layers.
Sandwiching a N-type layer between two p-type layers.

## Slide 4: How a “NPN” Transistor works?
Forward
backward
The base-emitter diode (forward) acts as a switch. when v1>0.7 it lets the electrons flow toward collector. so we can control our output current (Ic) with the input current (Ib) by using transistors.
C
B
E

## Slide 5
Collector
Emitter
Base
Transistors have three terminals:
Transistors work in 3 regions
Active: Always on
Ic=BIb
Saturation :Ic=Isaturation
On as a switch
Off :Ic=0
Off as a switch

## Slide 6
Transistor as a Switch
Transistors can be used as switches.1
Transistors can either
conduct or not conduct current.2
ie, transistors can either be on or off.2
Transistor
Switch

## Slide 7
Transistor Switching Example15
When VBE is less than 0.7V the transistor is off
and the lamp does not light.
When VBE is greater than 0.7V the transistor is on
and the lamp lights.
X
Variable
Voltage
Supply
12V

## Slide 8
Transistor Circuit : Light-Controlled Circuit
This transistor circuit contains
a Light-Dependent Resistor.
Because of the LDR, this circuit is dependent on light.
The purpose of this circuit is to turn on the LED when the light reaches a certain intensity.
Input = Voltage Divider
Process = Transistor
Output = LED
LED = Off.
Cover LDR.
RLDR .
VLDR .
Transistor switches on.
LED = On.

## Slide 9
Transistor as an amplifier:
Transistors are often used as amplifiers to increase input signal in radios, televisions and some other applications .The circuit may be designed to increase the current or voltage level.
The power gain is the product of current gain and voltage gain (P=V*I).

## Slide 10
Amplifier example:
As you see, the transistor is biased to be always on. The input signal is amplified by this circuit. The frequency of output is the same as its input, but the polarity of the signal is inverted.
The measure of amplification is the gain of transistor.
Example:
Input Amplitude =0.2v
Output amplitude=10v
Gain=10/0.2=50

## Slide 11
Field Effect Transistors
JFET
MOSFET
CMOS

## Slide 12
When the gate is negative ,it repels the electron in the N-channel. So there is no way for electrons to flow from source to drain.
When the negative voltage is removed from Gate ,the electrons can flow freely from source to drain .so the transistor is on.
How a JFET transistor works?

## Slide 13
When the Gate is positive voltage ,it allows electrons to flow from drain to source .In this case transistor is on.
In MosFET, the Gate is insulated from p-channel or n-channel. This prevents gate current from flowing, reducing power usage.
How a MOSFET Transistor works?

## Slide 14
Thank You !!
https://www.youtube.com/@AmelOline/videos
https://github.com/siagianp
https://github.com/amelcharolinesgn2/IoT_simulator-mqtt-NodeRed
https://github.com/amelcharolinesgn2/Cloud-Infrastructures
https://github.com/amelcharolinesgn2/ClouD-Infrastructure-SISKA-2025
Computer Vision
PDS
SDN
NFV