## Slide 1: 9.4_Transistors
Computer Vision
PDS
SDN
NFV
https://www.youtube.com/@AmelOline/videos
https://github.com/siagianp
https://github.com/amelcharolinesgn2/IoT_simulator-mqtt-NodeRed
https://github.com/amelcharolinesgn2/Cloud-Infrastructures
https://github.com/amelcharolinesgn2/ClouD-Infrastructure-SISKA-2025

## Slide 2: What is a transistor?

## Slide 3: What is a transistor?
A transistor is a 3 terminal electronic device made of semiconductor material.
Transistors have many uses, including amplification, switching, voltage regulation, and the modulation of signals

## Slide 4: Lecture Overview
What is a Transistor?
History
Types
Characteristics
Applications

## Slide 5: What is a Transistor?
Semiconductors: ability to change from conductor to insulator
Can either allow current or prohibit current to flow
Useful as a switch, but also as an amplifier
Essential part of many technological advances

## Slide 6: A Brief History
Guglielmo Marconi invents radio in 1895
Problem: For long distance travel, signal must be amplified
Lee De Forest improves on Fleming’s original vacuum tube to amplify signals
Made use of third electrode
Too bulky for most applications

## Slide 7: The Transistor is Born
Bell Labs (1947): Bardeen, Brattain, and Shockley
Originally made of germanium
Current transistors made of doped silicon

## Slide 8: How Transistors Work
Doping: adding small amounts of other elements to create additional protons or electrons
P-Type: dopants lack a fourth valence electron (Boron, Aluminum)
N-Type: dopants have an additional (5th) valence electron (Phosphorus, Arsenic)
Importance: Current only flows from P to N

## Slide 9: Diodes and Bias
Diode: simple P-N junction.
Forward Bias: allows current to flow from P to N.
Reverse Bias: no current allowed to flow from N to P.
Breakdown Voltage: sufficient N to P voltage of a Zener Diode will allow for current to flow in this direction.

## Slide 10
3 adjacent regions of doped Si (each connected to a lead):
  Base. (thin layer,less doped).
  Collector.
  Emitter.
2 types of BJT:
  npn.
  pnp.
Most common: npn (focus on it).
Bipolar Junction Transistor (BJT)
npn bipolar junction transistor
pnp bipolar junction transistor
Developed by Shockley (1949)

## Slide 11
1 thin layer of p-type, sandwiched between 2 layers of n-type.
N-type of emitter: more heavily doped than collector.
With VC>VB>VE:
  Base-Emitter junction forward biased, Base-Collector reverse biased.
  Electrons diffuse from Emitter to Base (from n to p).
  There’s a depletion layer on the Base-Collector junction no flow of e- allowed.
  BUT the Base is thin and Emitter region is n+ (heavily doped)  electrons have enough momentum to cross the Base into the Collector.
  The small base current IB controls a large current IC
BJT NPN Transistor

## Slide 12
Current Gain:
  α is the fraction of electrons that diffuse across the narrow Base region
  1- α is the fraction of electrons that recombine with holes in the Base region to create base current
The current Gain is expressed in terms of the β (beta) of the transistor (often called hfe by manufacturers).
β (beta) is Temperature and Voltage dependent.
It can vary a lot among transistors (common values for signal BJT: 20 - 200).
BJT characteristics

## Slide 13
Emitter is grounded.
Base-Emitter starts to conduct with VBE=0.6V,IC flows and it’s IC=b*IB.
Increasing IB, VBE slowly increases to 0.7V but IC rises exponentially.
As IC rises ,voltage drop across RC increases and VCE drops toward ground. (transistor in saturation, no more linear relation between IC and IB)
NPN Common Emitter circuit

## Slide 14
Common Emitter characteristics
No current flows
Collector current controlled by the collector circuit. (Switch behavior)
In full saturation VCE=0.2V.
Collector current proportional to Base current
The avalanche multiplication of current through collector junction occurs: to be avoided

## Slide 15
Operation Region | IB or VCE Char. | BC and BE Junctions | Mode
Cutoff | IB = Very small | Reverse & Reverse | Open Switch
Saturation | VCE = Small | Forward & Forward | Closed Switch
Active Linear | VCE = Moderate | Reverse & Forward | Linear Amplifier
Break-down | VCE = Large | Beyond Limits | Overload
Operation region summary

## Slide 16
BJT as Switch
Vin(Low ) < 0.7 V
  BE junction not forward biased
  Cutoff region
  No current flows
  Vout = VCE = Vcc
Vout = High
Vin(High)
  BE junction forward biased (VBE=0.7V)
  Saturation region
  VCE small (~0.2 V for saturated BJT)
  Vout = small
  IB = (Vin-VB)/RB
Vout = Low

## Slide 17
Basis of digital logic circuits
Input to transistor gate can be analog or digital
Building blocks for TTL – Transistor Transistor Logic
Guidelines for designing a transistor switch:
  VC>VB>VE
  VBE= 0.7 V
  IC independent from IB (in saturation).
  Min. IB estimated from by (IBmin» IC/b).
  Input resistance such that IB > 5-10 times IBmin because b varies among components, with temperature and voltage and RB may change when current flows.
  Calculate the max IC and IB not to overcome device specifications.
BJT as Switch 2

## Slide 18
Common emitter mode
Linear Active Region
Significant current Gain
Example:
Let Gain, b = 100
Assume to be in active region -> VBE=0.7V
Find if it’s in active region
BJT as Amplifier

## Slide 19
BJT as Amplifier
VCB>0 so the BJT is in active region

## Slide 20: Bipolar Transistor
A transistor is basically a Si or Ge crystal containing three separate regions.

## Slide 21: Architecture of BJTs
The bipolar junction transistor (BJT) is constructed with three doped semiconductor regions separated by two pn junctions
Regions are called emitter, base and collector

## Slide 22: Bipolar Transistor
The depletion layers do not have the same width, because different regions have different doping levels.

## Slide 23: Biasing
If both the junctions are forward biased free electrons enter the emitter and collector of the transistor, joins at the base and come out of the base.
If both the junction are reverse biased then small currents flows through both junctions only due to thermally produced minority carriers and surface leakage.

## Slide 24: Biasing
When the emitter junction is forward biased and collector junction is reverse biased then one expect large emitter current and small collector current but collector current is almost as large as emitter current.

## Slide 25: Transistor Current
The total current flowing into the transistor must be equal to the total current flowing out of it.

## Slide 26: Transistor Applications
Switching
Amplification
Variable Resistor
Impedance Matching
Voltage Regulation

## Slide 27: Basic circuits of BJT

## Slide 28: Operation of BJTs
BJT will operates in one of following four region
  Cutoff region (for digital circuit)
  Saturation region (for digital circuit)
  Linear (active) region (to be an amplifier)
  Breakdown region (always be a disaster)

## Slide 29: Operation of BJTs

## Slide 30: DC Analysis of BJTs
Transistor Currents:
IE = IC + IB
alpha (DC)
IC = DCIE
beta (DC)
IC = DCIB
  DC typically has a value between 20 and 200

## Slide 31: DC Analysis of BJTs
DC voltages for the biased transistor:
Collector voltage
VC = VCC - ICRC
Base voltage
VB = VE + VBE
  for silicon transistors, VBE = 0.7 V
  for germanium transistors, VBE = 0.3 V

## Slide 32: Q-point
The base current, IB, is established by the base bias
The point at which the base current curve intersects the dc load line is the quiescent or Q-point for the circuit

## Slide 33: Q-point

## Slide 34: DC Analysis of BJTs
The voltage divider biasing is widely used
Input resistance is:
RIN  DCRE
The base voltage is approximately:
VB  VCCR2/(R1+R2)

## Slide 35
Thank You !!
https://www.youtube.com/@AmelOline/videos
https://github.com/siagianp
https://github.com/amelcharolinesgn2/IoT_simulator-mqtt-NodeRed
https://github.com/amelcharolinesgn2/Cloud-Infrastructures
https://github.com/amelcharolinesgn2/ClouD-Infrastructure-SISKA-2025
Computer Vision
PDS
SDN
NFV